## Slide 1: Soil Water Balance Overview
University of Neuchâtel, Switzerland
Centre for Hydrogeology and Geothermics
December 16-20, 2019

## Slide 2
SWB – Modified Thornthwaite-Mather Soil-Water-Balance Code for estimating Water-Budget Components

## Slide 3: Thornthwaite and Mather: work originated with research on crop growth and yield at Seabrook Farms, New Jersey
Thornthwaite
Mather

## Slide 4
Modified from: Thornthwaite, 1948
Thornthwaite’s march oF
precipitation and potential evapotranspiration
Notes: From Thornthwaite’s commentary (1948):
In Brevard, N. C. (Fig.4-A), less than half an inch of water is needed in each of the winter months. The need rises rapidly during the spring, reaches a high point of more than 5 inches in July, and falls rapidly during the autumn. The total average annual water need is 28.50 inches. The precipitation ranges from less than 3.5 inches in November to more than 6.5 inches in July and is greater than the need in every month. The total average annual precipitation is 61.06 inches, more than twice the potential evapotranspiration.
In Louisville, Ky. (Fig.4-E), rainfall is fairly uniform through the year-between 3.5 and 4 inches a month except in autumn, when it falls below 3 inches. Since potential evapotranspiration is not uniform, however, there is a surplus of water in winter and a deficiency in summer, just as in North Head (Fig.4-D) and Seattle (Fig.4-F).
In Grand Junction, Colo. (Fig.4-R), rainfall is slight throughout the year. Water supply satisfies less than one-third of water need, and deficiency is very large. The climate is arid.

## Slide 5: SWB: Modified Thornthwaite-Mather water balance
Source: Thornthwaite and Mather, 1957
Potential evapotranspiration (PE)
Precipitation (P)
P – PE
Accumulated Pot. Water Loss
Soil storage
Actual evapotranspiration
Deficit
Surplus
Runoff
Snowmelt runoff

## Slide 6: Thornthwaite’s march of precipitation and potential evapotranspiration
“From a comparison of the seasonal march of precipitation with evapotranspiration, the magnitude of other related moisture parameters, the water surplus, water deficit, soil moisture storage, and water runoff may be determined.”
net infiltration (recharge),
Source: Thornthwaite and Mather, 1957

## Slide 7: how much moisture can be pulled from the soil?
Source: Thornthwaite and Mather, 1957
Accumulated Potential Water Loss (APWL)
Maximum Soil Moisture Capacity

## Slide 8: Runoff: SCS curve number
units are inches, of course!

## Slide 9: Continuous Frozen Ground Index
K=0.5 for above freezing conditions; K=0.08 if below freezing
A = 0.97
Source: Molnau and Bissel (1983)

## Slide 10: CFGI is used to increase runoff during frozen ground conditions to adjust curve number
Molnau and Bissel (1983) suggest starting with values of
56 and 83 for the LL and UL, respectively.

## Slide 11: Estimating the effect of irrigation
Source: Allen and others (1998), FAO Irrigation and drainage paper 56

## Slide 12: swb: irrigation demand
Source: Allen, R.G., Pereira, L.S., Raes, D. and Smith, M., 1998, Crop evapotranspiration-Guidelines for computing crop water requirements-FAO Irrigation and drainage paper 56: Rome, Food and Agriculture Organization of the United Nations, accessed May 5, 2011, at http://www.fao.org/docrep/X0490E/x0490e00.htm#Contents.

## Slide 13: crop ET calculation
Plant growth
Bare soil evap

## Slide 14: water stress coefficient Ks
Source: Allen and others (1998), FAO Irrigation and drainage paper 56

## Slide 15: effect of dual crop coefficient Kc
Source: Allen and others (1998), FAO Irrigation and drainage paper 56

## Slide 16: SWB methods and storage reservoirs

## Slide 17: Baseflow separation to estimate recharge

## Slide 18: Contributing area of gages used in baseflow separation

## Slide 19: Constraining Actual ET With “Observations” (if you got hella cash)
Credit: William Breiter, site US-Ro5
Credit: Christoph Vogel, site US-UMB
Credit: Charlie Krinsky, site US-RFE

## Slide 20: SWB data flow
Land Use
Water Content
Flow Direction
Hydrologic Soils Group
DayMet, PRISM, or other gridded PRECIPITATION, AIR TEMPERATURE
Irrigation
Recharge

## Slide 21: Evolution of SWB…
Dripps, W., 2003, The spatial and temporal variability of groundwater recharge within the Trout Lake basin of northern Wisconsin: United States -- Wisconsin, The University of Wisconsin - Madison.
https://github.com/smwesten-usgs/swb2

## Slide 22: SOIL WATER BALANCE 2.0
Same features as the original SWB plus:
Modules to simulate processes important to tropical island hydrology
Optimized for non-rectangular areas of interest
netCDF4 input and output
Geospatial transformations on-the-fly
Redesigned to allow for easier addition of new process modules
Crop irrigation demand estimated using FAO-56 methodology
SWB: Grid-based code designed to estimate potential groundwater recharge, taking full advantage of gridded land use, soils, and climate datasets.

## Slide 23
Little Plover River
Tomorrow / Waupaca River
(irrigation)
Bayfield Peninsula
State of Wisconsin
(in support of statewide
stream temperature modeling)
State of Minnesota
North Atlantic Coastal Plain
High Plains Aquifer
Elkhorn-Loupe
Appalachian Plateaus
(New York-Georgia)
Upper Colorado
River Basin
Hawaii Volcanic-Rock Aquifers
Floridan Aquifer
Oregon
Lakes
Water
Budget
Chippewa County
(frac sand mining)
Pacific Northwest Volcanic Aquifer System
State of Maine
Williston and Powder River Basins
Glacial Aquifers
Non-USGS applications:
Catalina Island, CA
Mexico
Brazil
Suriname
Spain
Nigeria
South Korea
Mississippi Alluvial Plain
Select SWB Application Sites in the U.S.: 2012-2018

## Slide 24: Running SWB for different areas of interest and different grid cell resolutions is easily done
1000-meter grid
100-meter grid
SWB inset model for Shellmound, Mississippi

## Slide 25: SWB-derived potential recharge 2000-2009
Deep percolation
in inches

## Slide 26: Example of FAO-56 crop water demand calculations with SWB
Estimated Irrigation
Amount (inches per year)
Potential Recharge
(inches per year)